## Slide 1: FANFAR: Reinforced cooperation to provide operational flood forecasting and alerts in West Africa
Aytor Naranjo, Lobelia/isardSAT
and the FANFAR consortium
Benin, Burkina Faso, Cap Verde, Chad, Gambia, Ghana, Guinea, Guinea-Bissau, Ivory Coast, Liberia, Mali, Mauretania, Niger, Nigeria, Senegal, Sierra Leone, Togo, NBA, VBA, OMVG, CBLT, ECOWAS, WMO
Notes: Acknowledge the FANFAR team & partners, mention also countries/organisations!

## Slide 2: Motivation
2020
Several floods in West Africa: 2020, 2019, 2018, 2017, 2016, 2012 …
Serious consequences: lives lost, economic damages, millions affected
Climate change  increased floods
Key need: accessible and up-to-date flood forecasts & alerts
2010
https://www.nytimes.com/2018/09/17/world/africa/nigeria-floods.html
2018
Notes: why

## Slide 3: The FANFAR project
Research & Innovation project financed by European Commission (2018-2021)
Vision
Resilient societies, minimum flood impacts, capable institutions
Forecasting system operated by regional & national West African institutions & partners
Overall aims
Provide a pre-operational flood forecasting & alert system at West African scale (updated every day)
Reinforce cooperation between West Africa and Europe  building system together!
Notes: what

## Slide 4: FANFAR objectives
Co-designed system
Co-developed system
Integrated system
Co-operated system
Accessible & timely system
Robust ICT
Sustainability
System should be:
Co-designed: working group defining prioritized needs
Co-adapted: jointly modified & developed according to needs
Integrated: all components working together
Co-operated: jointly operated and maintained
Provide reliable and timely access to information
Robust ICT, relevant for West African conditions (electricity, internet etc.)
Sustainably financed & maintained
Notes: Parable/liknelse: integrated system: car components, but also the road, the driver and the fuel

## Slide 5: Key achievements

## Slide 6: Co-design: what would a “good” system be?
4 workshops in West Africa & online
>30 organisations from 17 countries
Clarify & prioritize user needs with MCDA
Analyse behaviour & experiences
Abuja, 2020
Niamey, 2018
Notes: Add GENDER here # male/female?

## Slide 7
Stakeholders
Co-design: what would a “good” system be?
Objectives
Options
Priority: operational system > advanced features

## Slide 8: Operational flood forecasting & alert system for West Africa
Hydro model (rainfall-runoff):
  Niger-HYPE
  West Africa (WWH)
Initialisation/spin-up (blue)
  to get a state representing current conditions
  Need meteo. ’analysis’ (model + obs. of near-historic time, e.g. 30last days)
  Data assimilation (river flow, EO)
Forecast of future, using meteo forecasts (orange)
Information derivation
  Process output data to e.g. alerts (current conditions vs. relevant alert level thresholds for a given area)
Distribution
  One-way
  Two-way
  Simple to complex data
Operational production cloud platform (OPCP): scheduled, automated execution and monitoring = Hydrology-TEP
Openly accessible 1-10day forecasts
Updated every day since Sep. 2018
Developed jointly & continuously

## Slide 9: Distribution channels
Website
Email
SMS
Machine-to-machine API

## Slide 10: Local observations
Water level & discharge from local stations
Regular collection, formatting, quality control, FTP upload
Challenge: keep it operational
Contribution 2020

## Slide 11: Water level from satellite data

## Slide 12: Water level from satellite data
1078 virtual stations from multiple sattelite altimetry missions
Data since 2001, updated automatically
Ongoing validation with >30 local stations

## Slide 13: Hydrological modelling
Calibration & catchment delineation
Multiple models: WWH 1.3.5, Niger HYPE 2.30, West Africa HYPE 1.2
Assimilating local observations
Improved meteo. data cascade
Variables: streamflow, water levels, precipitation etc.
Daily forecast production
Recalibration
Assimilation
Catchment delination

## Slide 14: Flood risk information derivation
Flood thresholds:
  peak flow frequency (return periods)
  % of historic year
  Local thresholds
Impacts: population affected

## Slide 15: ICT platform for operational production
https://hydrology-tep.eu/
Automatized  code executed on cloud computing platform
Version control & standards
24/7 data flow & monitoring
Interactive processing
Community

## Slide 16: Capacity development & support
Hands-on training in workshops, in-depth courses, expert exchanges, bi-weekly meetings
Open multi-lingual training material & documentation: Knowledge base (wiki), YouTube, WhatsApp group, Forum, Help Desk, Email
MSc courses at AGRHYMET, PRESASS, ECOWAS DRR, UN-SPIDER
Nigeria, 2020
Sweden, 2019

## Slide 17: System performance & experience of West African agencies

## Slide 18: Forecast vs. reality: 2019
Reality: lives lost, displacements, damaged infrastructure etc.
Forecast performance: varied, good timing & location of peaks ( ± 1-2 days), underestimated peak magnitudes (-5-50%), minor false alarms

## Slide 19: Forecast vs. reality: Niamey, Niger, 2020
Consequences: 71 victims & 350 000 affected, 1441 ha agriculture, etc.
FANFAR performance: Timing & severity well captured, but duration underestimated
Collaborative evaluation by West African agencies and FANFAR partners live & retrospectively
www.slapis-niger.org , 2020-09-10
Local observations
Worst flood in 100 years

## Slide 20: Country-level feedback: Nigeria - NIHSA
Multiple institutions  harmonization efforts like FANFAR needed
Accurate severity levels at all stations (even if discharge magnitudes need to be improved)  FANFAR used by NIHSA since 2020
Component in annual budget
2020 flooding | 35/36 states affected
Consequences | 126 deaths, 48,114 persons displaced and 29,356 houses destroyed
Oct. 2020: Forecast: severity levels 1-3 in Kaduna & Niger Rivers 🡪 Reality: Flooding around Shiroro dam and Niger axis

## Slide 21: Experience of West African agencies 2020
Current accuracy of FANFAR
Very bad
Bad
Neutral
Good
Very good
Best
Worst
No
Yes
Future use if accuracy remains the same?
Overall likelihood of using FANFAR in future
“The system is good. However, the false alerts should be minimised“
“Problems with login to ICT platform”
“Great job done. Keep doing what you do best.”
Notes: Selected results, comprehensive analysis long/coming later.

## Slide 22: FANFAR already used beyond project
Regional scale: ECOWAS flood observatory
National scale: bulletins, social media, TV, newspapers to stakehodlers
Local scale: Sirba river EWS in Niger
Peace-keeping
UN MINUSMA, Mali
Notes: Mention prospects within VoltALARM and CREWS Togo

## Slide 23: Towards sustainability
Tandem agile approach:
  Operate current system  societal value
  Advance system & capacity
Capacity development: knowledge, know-how, gender balance
Collaboration: co-design, co-development & co-operation
Open: open-source tools, data, documentation & training
Accuracy & coverage: combination of observations and models across domain, continuous refinement, incorporate local knolwedge
Reliable access & production: web & SMS access, cloud ICT, up-to-date production, stable partners

## Slide 24: Current situation and way forward
Forecast produced in-house at SMHI since Jan 2022
EO-based water level data produced operationally in the whole basin with an unprecedented number of virtual stations
Actively looking for funding
Almost unique pre-operational service covering the Niger River basin and producing 1-10 day flood forecasts and alerts daily combining EO and in-situ
High social impact
Relatively low maintenance cost
Strong collaboration between stakeholders and willingness to have the system available

## Slide 25: THANK YOU!
Accra, 2019
Abuja, 2020
Niamey, 2018
Norrköping, 2018
Online, 2021