## Slide 1
Water products under Copernicus:
Land monitoring
Emergency
&
Water-ForCE webinar “Copernicus for Africa”
Presented by Milan Kalas on behalf of the CEMS & CLMS 30 March 2022

## Slide 2: Copernicus
EU's Earth Observation Programme

## Slide 3
Existing water-related products and services under CEMS
For Whom?
  European Emergency Response Coordination Centre (ERCC)
  Global Disaster Alert and Coordination System (GDACS)
  International aid organizations, EEAS, UNCCD, etc.

## Slide 4: On-Demand Mapping – Water products
Rapid Mapping: fast provision of products (hours to a few days) with the aim to support emergency response
CEMS on-demand Mapping
(Authorised user needs to request product)
Water-related products:
Flood extent and impact maps
Historical flood delineation
Tsunami risk assessment
Risk and Recovery Mapping: products available usually within a few weeks with the aim to support risk prevention and recovery efforts
https://emergency.copernicus.eu/mapping/
Post-event analysis
Rapid mapping of flooded areas
Tropical Cyclone Eloise 22-23 January 2021, Mozambique

## Slide 5: CEMS Flood forecast and monitoring service
GloFAS = Global Flood Awareness System
GFM = Global Flood Monitoring
GloFAS and GFM provide:
Global hydrological ensemble forecasts updated daily
Highlights of expected flooding and associated flood risk level over next 30 days
Seasonal hydrological outlook showing wet/dry anomalies over next 16 weeks
Global, SAR-based, flood monitoring with timeliness of >8hours and revisit frequency of 3-12 days at 20m resolution (under dev.)
Map products and datasets through dedicated web and data services
https://www.globalfloods.eu/

## Slide 6: CEMS Drought monitoring service
GDO provides
  Early warning, monitoring and forecasting of droughts and their likely impacts, based on satellite data, hydro-meteorological modelling and in-situ observations.
  Based on a conceptual model of drought risk
GDO = Global Drought Observatory
https://edo.jrc.ec.europa.eu/

## Slide 7
Water Bodies global 10-day 100m
Lake Surface Water Temperature global (min 1000lakes) 10day 1km
Lake Water Quality global (4264 lakes) 10day/month 300m /100m
Lake and River Water level global (>10000 stations) 10day/monthly
Current: Monthly global 100m dynamics (within mask)
GSWE: yearly updates (JRC) with Landsat
Future: uptake GSWE in operational portfolio as WB product
GSWE - algorithm adaptation for S2
quality control
documentation
[2yrs]
Water Bodies 100m>20m
Water Products

## Slide 8: Africa Inland Water Coverage
Country | No. of lakes
Algeria | 5
Angola | 4
Benin | 2
Botswana | 3
Burkina Faso | 2
Burundi | 1
Cameroon | 5
Chad | 8
Democratic Republic of the Congo | 17
Djibouti | 1
Egypt | 11
Ethiopia | 15
Gabon | 7
Ghana | 7
Guinea | 1
Ivory Coast | 5
Kenya | 5
Madagascar | 5
Malawi | 3
Mali | 8
Mauritania | 1
Morocco | 4
Mozambique | 12
Namibia | 1
Nigeria | 9
Rwanda | 4
Senegal | 2
Somalia | 1
South Africa | 13
South Sudan | 2
Sudan | 5
Togo | 2
Tunisia | 1
Uganda | 8
United Republic of Tanzania | 15
Zambia | 12
Zimbabwe | 2

## Slide 9: Water Quality for SDG 6.
Lake Turkana, Kenya
Turbidity data over 10 years
seasonal trends
NRT Turbidity data - 2018
Water Quality product: +-4500 lakes at 300m (turbidity, trophic state, reflectance)
Spatial resolution
  300m, 1km, 100m (in evolution)
Temporal aggregation
  10days for water LSWT, TUR and TSI
Time span
  2002-2012 (MERIS + AATSR) –
  2016-ongoing (OLCI + SLSTR)
Parameters
  Lake Surface Water Temperature (LSWT)
  Turbidity (TUR)
  Trophic State Index (TSI)
  Lake Surface Reflectances (LSR)

## Slide 10
Current: 10000+ virtual stations
Future: adding S6
Expanding no of stations
Water Bodies global 10-day 100m
Lake Surface Water Temperature global (min 1000lakes) 10day 1km
Lake Water Quality global (4264 lakes) 10day/month 300m /100m
Lake and River Water level global (>10000 stations) 10day/monthly
Water Products

## Slide 11
All services and products presented are free and open for everyone!
https://emergency.copernicus.eu/
Land monitoring
Emergency
&
https://land.copernicus.eu/